Transistor de Efeito de Campo Metal-Óxido Semicondutor
MOS Field-Effect
Transistors (MOSFETs)‏

---
MOSFETs: Tipos
- Tipo enriquecimento (ou indução)
  - Canal N
  - Canal P
- Tipo empobrecimento (ou depleção)
  - Canal N
  - Canal P

---
Estrutura física
MOSFET tipo enriquecimento canal N
[Speaker Notes: sedr42021_0401a.jpg]

---
Tensão positiva aplicada à porta de um MOSFET tipo enriquecimento.
[Speaker Notes: sedr42021_0402.jpg]

---
Transístor MOSFET com vGS > Vt e com vDS . O dispositivo se comporta como um resistor controlado por tensão ( vGS)
[Speaker Notes: sedr42021_0403.jpg]

---
Características iD–vDS do MOSFET como resistor controlado por tensão.
[Speaker Notes: sedr42021_0404.jpg]

---
Operação do MOSFET com vDS alto. O canal começa a adquirir uma forma de estrangulamento próximo ao dreno. A resistência do dispositivo aumenta com o aumento de vDS , para um vGS constante e maior que Vt.
[Speaker Notes: sedr42021_0405.jpg]

---
O efeito do aumento de vDS: : o canal vai se estrangulando perto do dreno. Com vDS acima de vGS – Vt , o aumento da tensão de dreno praticamente não causa mais efeito.
[Speaker Notes: sedr42021_0407.jpg]

---
iD versus vDS com vGS > Vt.
[Speaker Notes: sedr42021_0406.jpg]

---
Símbolos
MOSFET tipo enriquecimento.
[Speaker Notes: sedr42021_0410a.jpg]

---
Regiões de operação.
[Speaker Notes: sedr42021_0411a.jpg]

---
Regiões de operação.
Região de corte
v_{GS} < V_t
Região triodo
v_{GS} > V_t, v_{DS} < v_{GS} - V_t
Região de saturação
v_{GS} > V_t, v_{DS} >= v_{GS} - V_t
[Speaker Notes: sedr42021_0411a.jpg]

---
Característica iD–vGS de um MOSFET canal N tipo enriquecimento.
[Speaker Notes: sedr42021_0412.jpg]

---
Modelo para grandes sinais na região de saturação.
[Speaker Notes: sedr42021_0413.jpg]

---
Regiões de Operação
Níveis de tensão dos terminais de um MOSFET canal N tipo enriquecimento e suas regiões de operação.
[Speaker Notes: sedr42021_0414.jpg]

---
O efeito da modulação de comprimento de canal
[Speaker Notes: sedr42021_0416.jpg]

---
Equações do MOSFET canal N

---
Modelo para grandes sinais
[Speaker Notes: sedr42021_0417.jpg]

---
MOSFET Tipo Enriquecimento Canal P
Símbolos
[Speaker Notes: sedr42021_0418a.jpg]

---
Polarização
[Speaker Notes: sedr42021_0418a.jpg]

---
Regiões de Operação
[Speaker Notes: sedr42021_0419.jpg]

---
Equações do MOSFET Canal P

---
MOSFET tipo enriquecimento: canais N e P
[Speaker Notes: sedr42021_tb0401a.jpg]

---
Parâmetros dos MOSFETs

---
Figure E4.8
[Speaker Notes: sedr42021_e0408.jpg]

---
Figure 4.20 Circuit for Example 4.2.
[Speaker Notes: sedr42021_0420.jpg]

---
Figure 4.21 Circuit for Example 4.3.
[Speaker Notes: sedr42021_0421.jpg]

---
Figure E4.12
[Speaker Notes: sedr42021_e0412.jpg]

---
Figure 4.22 Circuit for Example 4.4.
[Speaker Notes: sedr42021_0422.jpg]

---
Figure 4.23 (a) Circuit for Example 4.5. (b) The circuit with some of the analysis details shown.
[Speaker Notes: sedr42021_0423a.jpg]

---
Figure 4.24 Circuit for Example 4.6.
[Speaker Notes: sedr42021_0424.jpg]

---
Figure 4.25 Circuits for Example 4.7.
[Speaker Notes: sedr42021_0425a.jpg]

---
Figure E4.16
[Speaker Notes: sedr42021_e0416.jpg]

---
Figure 4.26 (a) Basic structure of the common-source amplifier. (b) Graphical construction to determine the transfer characteristic of the amplifier in (a).
[Speaker Notes: sedr42021_0426a.jpg]

---
Figure 4.26 (Continued) (c) Transfer characteristic showing operation as an amplifier biased at point Q.
[Speaker Notes: sedr42021_0426c.jpg]

---
Figure 4.27 Two load lines and corresponding bias points. Bias point Q1 does not leave sufficient room for positive signal swing at the drain (too close to VDD). Bias point Q2 is too close to the boundary of the triode region and might not allow for sufficient negative signal swing.
[Speaker Notes: sedr42021_0427.jpg]

---
Figure 4.28 Example 4.8.
[Speaker Notes: sedr42021_0428a.jpg]

---
Figure 4.28 (Continued)‏
[Speaker Notes: sedr42021_0428b.jpg]

---
Figure 4.29 The use of fixed bias (constant VGS) can result in a large variability in the value of ID. Devices 1 and 2 represent extremes among units of the same type.
[Speaker Notes: sedr42021_0429.jpg]

---
Figure 4.30 Biasing using a fixed voltage at the gate, VG, and a resistance in the source lead, RS: (a) basic arrangement; (b) reduced variability in ID; (c) practical implementation using a single supply; (d) coupling of a signal source to the gate using a capacitor CC1; (e) practical implementation using two supplies.
[Speaker Notes: sedr42021_0430a.jpg]

---
Figure 4.31 Circuit for Example 4.9.
[Speaker Notes: sedr42021_0431.jpg]

---
Figure 4.32 Biasing the MOSFET using a large drain-to-gate feedback resistance, RG.
[Speaker Notes: sedr42021_0432.jpg]

---
Figure 4.33 (a) Biasing the MOSFET using a constant-current source I. (b) Implementation of the constant-current source I using a current mirror.
[Speaker Notes: sedr42021_0433a.jpg]

---
Figure 4.34 Conceptual circuit utilized to study the operation of the MOSFET as a small-signal amplifier.
[Speaker Notes: sedr42021_0434.jpg]

---
Figure 4.35 Small-signal operation of the enhancement MOSFET amplifier.
[Speaker Notes: sedr42021_0435.jpg]

---
Figure 4.36 Total instantaneous voltages vGS and vD for the circuit in Fig. 4.34.
[Speaker Notes: sedr42021_0436.jpg]

---
Figure 4.37 Small-signal models for the MOSFET: (a) neglecting the dependence of iD on vDS in saturation (the channel-length modulation effect); and (b) including the effect of channel-length modulation, modeled by output resistance ro = |VA| /ID.
[Speaker Notes: sedr42021_0437a.jpg]

---
Figure 4.38 Example 4.10: (a) amplifier circuit; (b) equivalent-circuit model.
[Speaker Notes: sedr42021_0438a.jpg]

---
Figure 4.39 Development of the T equivalent-circuit model for the MOSFET. For simplicity, ro has been omitted but can be added between D and S in the T model of (d).
[Speaker Notes: sedr42021_0439.jpg]

---
Figure 4.40 (a) The T model of the MOSFET augmented with the drain-to-source resistance ro. (b) An alternative representation of the T model.
[Speaker Notes: sedr42021_0440a.jpg]

---
Figure 4.41 Small-signal equivalent-circuit model of a MOSFET in which the source is not connected to the body.
[Speaker Notes: sedr42021_0441a.jpg]

---
Table 4.2
[Speaker Notes: sedr42021_tb0402a.jpg]

---
Figure 4.42 Basic structure of the circuit used to realize single-stage discrete-circuit MOS amplifier configurations.
[Speaker Notes: sedr42021_0442.jpg]

---
Figure E4.30
[Speaker Notes: sedr42021_e0430a.jpg]

---
Table 4.3
[Speaker Notes: sedr42021_tb0403a.jpg]

---
Figure 4.43 (a) Common-source amplifier based on the circuit of Fig. 4.42. (b) Equivalent circuit of the amplifier for small-signal analysis. (c) Small-signal analysis performed directly on the amplifier circuit with the MOSFET model implicitly utilized.
[Speaker Notes: sedr42021_0443a.jpg]

---
Figure 4.44 (a) Common-source amplifier with a resistance RS in the source lead. (b) Small-signal equivalent circuit with ro neglected.
[Speaker Notes: sedr42021_0444a.jpg]

---
Figure 4.45 (a) A common-gate amplifier based on the circuit of Fig. 4.42. (b) A small-signal equivalent circuit of the amplifier in (a). (c) The common-gate amplifier fed with a current-signal input.
[Speaker Notes: sedr42021_0445a.jpg]

---
Figure 4.46 (a) A common-drain or source-follower amplifier. (b) Small-signal equivalent-circuit model. (c) Small-signal analysis performed directly on the circuit. (d) Circuit for determining the output resistance Rout of the source follower.
[Speaker Notes: sedr42021_0446a.jpg]

---
Table 4.4
[Speaker Notes: sedr42021_tb0404a.jpg]

---
Table 4.4 (Continued)‏
[Speaker Notes: sedr42021_tb0404c.jpg]

---
Figure 4.47 (a) High-frequency equivalent circuit model for the MOSFET. (b) The equivalent circuit for the case in which the source is connected to the substrate (body). (c) The equivalent circuit model of (b) with Cdb neglected (to simplify analysis).
[Speaker Notes: sedr42021_0447a.jpg]

---
Figure 4.48 Determining the short-circuit current gain Io /Ii.
[Speaker Notes: sedr42021_0448.jpg]

---
Table 4.5
[Speaker Notes: sedr42021_tb0405.jpg]

---
Figure 4.49 (a) Capacitively coupled common-source amplifier. (b) A sketch of the frequency response of the amplifier in (a) delineating the three frequency bands of interest.
[Speaker Notes: sedr42021_0449a.jpg]

---
Figure 4.50 Determining the high-frequency response of the CS amplifier: (a) equivalent circuit; (b) the circuit of (a) simplified at the input and the output;
[Speaker Notes: sedr42021_0450a.jpg]

---
Figure 4.50 (Continued) (c) the equivalent circuit with Cgd replaced at the input side with the equivalent capacitance Ceq; (d) the frequency response plot, which is that of a low-pass single-time-constant circuit.
[Speaker Notes: sedr42021_0450c.jpg]

---
Figure 4.51 Analysis of the CS amplifier to determine its low-frequency transfer function. For simplicity, ro is neglected.
[Speaker Notes: sedr42021_0451.jpg]

---
Figure 4.52 Sketch of the low-frequency magnitude response of a CS amplifier for which the three break frequencies are sufficiently separated for their effects to appear distinct.
[Speaker Notes: sedr42021_0452.jpg]

---
Figure 4.53 The CMOS inverter.
[Speaker Notes: sedr42021_0453.jpg]

---
Figure 4.54 Operation of the CMOS inverter when vI is high: (a) circuit with vI = VDD (logic-1 level, or VOH); (b) graphical construction to determine the operating point; (c) equivalent circuit.
[Speaker Notes: sedr42021_0454a.jpg]

---
Figure 4.55 Operation of the CMOS inverter when vI is low: (a) circuit with vI = 0 V (logic-0 level, or VOL); (b) graphical construction to determine the operating point; (c) equivalent circuit.
[Speaker Notes: sedr42021_0455a.jpg]

---
Figure 4.56 The voltage transfer characteristic of the CMOS inverter.
[Speaker Notes: sedr42021_0456.jpg]

---
Figure 4.57 Dynamic operation of a capacitively loaded CMOS inverter: (a) circuit; (b) input and output waveforms; (c) trajectory of the operating point as the input goes high and C discharges through QN; (d) equivalent circuit during the capacitor discharge.
[Speaker Notes: sedr42021_0457a.jpg]

---
Figure 4.58 The current in the CMOS inverter versus the input voltage.
[Speaker Notes: sedr42021_0458.jpg]

---
Figure 4.59 (a) Circuit symbol for the n-channel depletion-type MOSFET. (b) Simplified circuit symbol applicable for the case the substrate (B) is connected to the source (S).
[Speaker Notes: sedr42021_0459a.jpg]

---
Figure 4.60 The current-voltage characteristics of a depletion-type n-channel MOSFET for which Vt = –4 V and kn(W/L) = 2 mA/V2: (a) transistor with current and voltage polarities indicated; (b) the iD–vDS characteristics; (c) the iD–vGS characteristic in saturation.
[Speaker Notes: sedr42021_0460a.jpg]

---
Figure 4.61 The relative levels of terminal voltages of a depletion-type NMOS transistor for operation in the triode and the saturation regions. The case shown is for operation in the enhancement mode (vGS is positive).
[Speaker Notes: sedr42021_0461.jpg]

---
Figure 4.62 Sketches of the iD–vGS characteristics for MOSFETs of enhancement and depletion types, of both polarities (operating in saturation). Note that the characteristic curves intersect the vGS axis at Vt. Also note that for generality somewhat different values of |Vt| are shown for n-channel and p-channel devices.
[Speaker Notes: sedr42021_0462.jpg]

---
Figure E4.51
[Speaker Notes: sedr42021_e0451.jpg]

---
Figure E4.52
[Speaker Notes: sedr42021_e0452.jpg]

---
Figure 4.63 Capture schematic of the CS amplifier in Example 4.14.
[Speaker Notes: sedr42021_0463.jpg]

---
Figure 4.64 Frequency response of the CS amplifier in Example 4.14 with CS = 10 F and CS = 0 (i.e., CS removed).
[Speaker Notes: sedr42021_0464.jpg]

---
Figure P4.18
[Speaker Notes: sedr42021_p04018a.jpg]

---
Figure P4.33
[Speaker Notes: sedr42021_p04033a.jpg]

---
Figure P4.36
[Speaker Notes: sedr42021_p04036.jpg]

---
Figure P4.37
[Speaker Notes: sedr42021_p04037.jpg]

---
Figure P4.38
[Speaker Notes: sedr42021_p04038.jpg]

---
Figure P4.41
[Speaker Notes: sedr42021_p04041.jpg]

---
Figure P4.42
[Speaker Notes: sedr42021_p04042a.jpg]

---
Figure P4.43
[Speaker Notes: sedr42021_p04043a.jpg]

---
Figure P4.44
[Speaker Notes: sedr42021_p04044a.jpg]

---
Figure P4.45
[Speaker Notes: sedr42021_p04045.jpg]

---
Figure P4.46
[Speaker Notes: sedr42021_p04046a.jpg]

---
Figure P4.47
[Speaker Notes: sedr42021_p04047.jpg]

---
Figure P4.48
[Speaker Notes: sedr42021_p04048.jpg]

---
Figure P4.54
[Speaker Notes: sedr42021_p04054.jpg]

---
Figure P4.61
[Speaker Notes: sedr42021_p04061.jpg]

---
Figure P4.66
[Speaker Notes: sedr42021_p04066.jpg]

---
Figure P4.74
[Speaker Notes: sedr42021_p04074.jpg]

---
Figure P4.75
[Speaker Notes: sedr42021_p04075.jpg]

---
Figure P4.77
[Speaker Notes: sedr42021_p04077.jpg]

---
Figure P4.86
[Speaker Notes: sedr42021_p04086.jpg]

---
Figure P4.87
[Speaker Notes: sedr42021_p04087.jpg]

---
Figure P4.88
[Speaker Notes: sedr42021_p04088a.jpg]

---
Figure P4.97
[Speaker Notes: sedr42021_p04097.jpg]

---
Figure P4.99
[Speaker Notes: sedr42021_p04099.jpg]

---
Figure P4.101
[Speaker Notes: sedr42021_p04101.jpg]

---
Figure P4.104
[Speaker Notes: sedr42021_p04104.jpg]

---
Figure P4.117
[Speaker Notes: sedr42021_p04117.jpg]

---
Figure P4.120
[Speaker Notes: sedr42021_p04120.jpg]

---
Figure P4.121
[Speaker Notes: sedr42021_p04121a.jpg]

---
Figure P4.123
[Speaker Notes: sedr42021_p04123.jpg]